## Slide 1: LAB 3: Pipelined Machine
Moinuddin K Qureshi

## Slide 2
Announcements
Gist of the mid semester class survey:
  We seem to be doing okay with lectures/exams
  Would be nice to have a 3-5 min break during the lecture
  Labs are tough (35/45)  We learn a lot, but need more help
  Split the lab into two or more parts, with staggered deadline
  Verilog/VHDL instead of C  Will increase debug time by ~4x
Lab 3 is split into two parts:
  Microcode due this Friday
  Datapath due on Tuesday
  We will provide a test harness and test cases for the datapath
We will go over the Pipeline lab today, and get started with Caches

## Slide 3
Warning!!
This course requires heavy programming
We assume you are already comfortable with C programming (4 Labs, all in C)
If you do not have the right programming skills, these labs will take forever
“For a 3 hour credit class, I was spending nearly ~40 hours on each assignment.”
“In many assignments, there were times where I needed to write over 1000+ or 2000+ lines of code.”
“Because I had an error in 5 or 6 lines, I got a 20% on it. This was extremely unfair.”
“Most of the effort involved went into debugging extremely complex C code.”

## Slide 4
Lab1 as touchstone (5% of grade)
Already posted on T-square, due this Friday 1pm
A shortened version of one of the labs
Should take about 3-4 hours (and ~150 lines) for solution
We will provide a test harness so that you know what score to expect from your submission
If you find yourself spending 10+ hours or writing more than 1000 lines of code, and still not getting the right score, you may not have the right programming background  rethink about taking this course
Note: No collaboration, you cannot look at each other’s code.
Cheating Cases Dealt Seriously: course grade drop + report to dean

## Slide 5
Unfortunately …
It has come to our attention that some students obtained solution from unauthorized means: previous years, online, other students
We will check all Lab 2/Lab 3 submissions with plagiarism detection script:
Measure of Software Similarity (MOSS): http://theory.stanford.edu/~aiken/moss/
Detects “substantial” similarity in code (robust to naming/spacing)
In last three years, out of 40 detections, not a single student contested
If you obtained the code by unauthorized means, you have two choices:
(a) By this Friday, withdraw your Lab2 – no questions asked, will have option for re-grade for 50% of the assignment credit after Midterm 2
(b) If not, and if we detect plagiarism:
Zero on the lab assignment (no option for Re-grade)
+ One grade drop in the final course grade
+ Reporting to the dean of students (goes as academic warning in file)

## Slide 6: LAB 3: Pipelined Machine

## Slide 7: Overview

## Slide 8: FETCH Stage

## Slide 9: DECODE Stage

## Slide 10: AGEX Stage

## Slide 11: MEM Stage

## Slide 12: STORE RESULT (WRITEBACK) Stage

## Slide 13
How to go about doing the Lab?
Writing software is an art, as much it is engineering
Break complex task into smaller (easier) sub tasks:
  Write Microcode for all instructions (become familiar with design)
  Model the datapath without any dependencies (No stalls  LD=1)
    Assume branches are never taken
    Cache always gives R=1 (change %13 or %9 to %1)
    No data dependencies (test instructions without data dep)
    Can still have bubbles when the pipeline is filling up  VLD=0
  Now start adding the stalls
    Add the memory related stalls (cache gives R=0, back to %13)
    Data Dependencies (RAW only, why?)
    Branch stalls (fetch is stalled for control flow instructions)

## Slide 14: Control Store: Regulates Pipeline
64 rows x 23 columns
64 rows x 23 columns (signals needed in different stages, colored)
Indexed by 6 bits { IR[15:12], IR[11], IR[5] }  {OPCODE X Y}

## Slide 15: Consider the ADD instruction
For the ADD instruction, the opcode is 0001
ADD comes in two flavors: REG (IR[5]=0) or Immediate (IR[5]=1)
IR[11] is not a steering bit for ADD, so ADD should do the same
thing irrespective of whether IR[11] is 0 or 1
ADD will map to four rows:
0001 00  Row 4  ADD REG (IR[11] happens to be 0)
0001 01  Row 5  ADD IMM(IR[11] happens to be 0)
0001 10  Row 6  ADD REG ( IR[11] happens to be 1)
0001 11  Row 7  ADD IMM( IR[11] happens to be 1)
COPY

## Slide 16: Row 4, ADD REG (IR[11]=0)
64 rows x 23 columns
This ADD instruction needs to read both REGs
DECODE: SR1 is needed (1) and SR2 is needed (1)
AGEX: ALU RESULTMUX should select ALU and not SHFT (1)
SR: DR VALUE should come from ALU result (11)
This instruction writes to REG (LDREG) and condition code (LDCC)
1
1
1
1
1
1
1
Note: ALUK=00 is ADD by default

## Slide 17: Row 5, ADD IMM(IR[11]=0)
64 rows x 23 columns
This ADD instruction needs only SR1, so two changes:
DECODE: SR1 is needed (1) and SR2 is needed (0)
AGEX: SR2MUX should get value from SEXT(imm5)  1
(other signals same as Row 4)
1
1
1
1
1
1
1
1
0
1
1
1
1
1
1

## Slide 18: Row 6 is IDENTICAL to Row 4 Row 7 is IDENTICAL to Row 5
Hint: XOR and AND should be quite easy now

## Slide 19
Datapath: No stalls, dependencies
Consider ADD R0, R1, R2
Cycle: 1

## Slide 20
DECODE: No stalls, dependencies
Consider ADD R0, R1, R2
Cycle: 2
IGNORE FOR RIGHT NOW

## Slide 21
AGEX: No stalls, dependencies
Consider ADD R0, R1, R2
Cycle: 3

## Slide 22
MEM: No stalls, dependencies
Consider ADD R0, R1, R2
Cycle: 4
Why is there no LD.SR?

## Slide 23
SR: No stalls, dependencies
Consider ADD R0, R1, R2
Cycle: 5
Actual writing to REGFILE
Must happen in DECODE stage in cycle 5

## Slide 24
Now Add Dependencies and Stalls
1. Cache not ready (in FETCH and MEM)  stall, and insert bubble
2. Data dependencies (check inputs to block in DECODE stage)
3. Control dependencies (Decoded a control instruction? stall fetch)